## Slide 1: Machine Learning on a Raspberry Pi
Linda MacPhee-Cobb
https://github.com/timestocome
Notes: Introduce self, background, interests
Please interrupt, ask questions….

## Slide 2: Mobile Robots
Sensors: UltraSonic distance sensor, Camera
Trained using Google’s TF Mobile Models
Obstacle avoidance with simple RL
Output: Wheel movement f/r, turn servo to steer, LED lights if either cat is spotted
kits available: Frye’s Amazon eBay…
Notes: Robot kits available Frye’s, eBay, Amazon
More expensive ones require less soldering and have better directions
MicroCenter and EPO also have lots of parts

## Slide 3: Image classification
Out of the box Google Mobile Network recognizes many objects ~ 10secs/frame
Re-trained on smaller sets ( both cats ) runs ~ 2 frames/second
~100 images each category, 3 categories (Min, Merlin, No cat)
~30 mins on desktop, copy trained network onto Pi
* when you retrain it the built in classifications are forgotten
Notes: Google has made TF and several pre-trained models available for mobile devices and SBC
Re-train on your desktop, drop model on to Pi after training
Simple models are very fast, slow ones still good for package on porch, dog on couch, garage door open
Open CV is also available for Raspberry Pi

## Slide 4: Using Tensorflow on a Pi
Change the default system Python to 3.5
Follow the directions to install TF on a Pi
https://github.com/samjabrahams/tensorflow-on-raspberry-pi/
* Change the name of the wheel file to cp35-cp35m from cp34-cp34
Step by step detailed directions on
https://github.com/timestocome/RaspberryPi-Robot

## Slide 5: Building an object detector
Download and install TensorFlow models on your desktop and Pi
https://github.com/tensorflow/models
Install and Test the default model on your Pi
https://github.com/tensorflow/models/tree/master/research/object_detection
Take and image and try it out
https://github.com/timestocome/RaspberryPi-Robot/tree/master/ObjectDetection

## Slide 6: Build a grey cat orange cat detector
Detailed directions and help
https://github.com/timestocome/RaspberryPi-Robot/tree/master/catID
You’ll need Python, Tensorflow and the TF mobile models
installed on your desktop and Pi
Collect images ( ~100 orange cat, ~100 grey cat, ~ 100 not a cat )
Put orange cat images, grey cat, not a cat images into 3 different directories
Try different models, you’l be trading speed and accuracy
Copy the saved model to your Pi
Test

## Slide 7: Tensorflow Resources
Tensorflow for Poets
https://codelabs.developers.google.com/codelabs/tensorflow-for-poets/#0

## Slide 8: Self teaching
Using a small state space and one objective RL is easy
Multiple objectives is mostly unsolved
Sensor data comes in fast, use lean code and models
Notes: Wheels are deliberately pulsed after first robot beheaded itself under couch and was then finished off by Merlin
Robot is sensing me in it’s way and adjusting
Proto type, robot relearns every time I start it, not currently saving data
Sensor data comes in fast, code must be lean

## Slide 9: Simple Reinforcement Learning
The Pi’ll be taking sensor data at high speeds
( and in large amounts if you’re using video )
Start with random values
Every time the sensor data comes back into the range in your matrices
select the action with the highest value. If things get better increase that value, else decrease it

## Slide 10: UltraSonic Distance Sensor
AI and ML Robotics Group ( Stanford ) trained several robots to map rooms
using SLAM
Bumped into a RE Agent at EPO who was using these sensors to create floor plans
by following walls
Car robot learns obstacle avoidance in about 100-1000 time steps, trick is to use
a small state space matrix (actions, distance)
Notes: SR204 UltraSonic distance sensor
sends ultra sonic pulse out, gets reflected signal back at speed of sound ~344 m/s 15’-1”
know the limits of your sensor
check spec sheets, incoming data may need manipulation ( temp/humidity )

## Slide 11: Artificial Intelligence
Before AlphaGo there was Blondie24
Everything AlphaGo does is in this book and
a few things it doesn’t yet do
Blondie24 played world class checkers on
mid 1990s computers that were no more
powerful than a Raspberry Pi
Notes: Blondie used all the Google Brain techniques: Markov tree search, neural networks, self play, also used evolutionary computing which is coming back into use
Very readable book, highly recommend

## Slide 12: Sensor notes
Many sensors were developed for Arduino which takes
up to 5V input, Pi max is 3.3V so ~2V is sent to ground using
resistors
Amps are how much ( think of a tank of water)
Volts are the power (think water pressure coming out of hose)
Resistors can split voltage into different wires (hoses)
Always check the spec sheets for sensors, data may need manipulation to be useful
Most sensors have been optimized for hardware not software